# FB031  |  Lay-in system with picture rail trim

| Pos............................ ..............................m² Pos............................ Pos............................ ..................running m | Delivery and installation of durlum metal panels of the System FB031. The metal panels are cut to fit in the picture rail [see separate position] on one side to compensate for tolerance and slid in. On the other side, the panel is laid form-fitting and tension-free on the profile. Easy demounting without tools is ensured. Tolerances and quality requirements according to TAIM, DIN EN 13964 and durlum Standards. Material: Optionally galvanised steel or aluminium/stainless steel Thickness: According to strength requirements Surface finish: D206-700 white powder coated similar to RAL 9016, optional colour RAL ............... Coating thickness: Approx. 70 µm Perforations: durlum Type RG-L15 [2.5/5.5] Sound absorption: By means of a special durlum acoustic fleece s=approx. 0.73, optionally in black or white Dimensions: Length ............... mm Width ............... mm €/m² Start-up costs depending on format, training and call-up € Delivery and installation of durlum 031 picture rails of aluminium. The profiles are to be attached horizontally on the wall. Only officially approved dowels many be used. The spacing of the attachment points is according to DIN 18168, DIN EN 13964 and the loads of the system and to be checked by the contractor. The metal panels are cut off at the end on the one side of the corridor to compensate for tolerance and slid into the lip of the picture rail and, on the other side of the corridor, laid in front of the lip. Exact fitting is to be observed! Between the corridor walls and lower edge of the picture rail, a covered gap exists in which pictures, etc. can be hung with special hooks. It is only permissible to use structure components that have been approved by the manufacturer of the metal panels. Material thickness: 1.5 mm Surface finish: D206-700 white powder coated similar to RAL 9016, optional colour RAL ............... Profile form: According to durlum 031 with closed gap €/running m |
| --- | --- |